## Slide 1: Robotic palletizing cell — gripper-close fault A-301 at step 30
Technical use case
Infeed conveyor
case arrives
B11 pick photo-eye
Robot to pick
S20 · robot at pick
position confirmed
Gripper close · S30
Y4 valve → jaws
B21 must confirm ≤ 1.5 s
Place on pallet
S40 · layer pattern
light curtain clear
Return home
S50 · next cycle
PLC sequence controller
checks each step condition · enforces interlocks (light curtain, robot home, air pressure) · raises alarms
What the PLC sees at the stop
Y4 close command
ON
B21 closed feedback
OFF
Condition timeout
1.5 s exceeded
Result
A-301 · cell FAULT at S30
ARIA
Candidate causes from the fault model
B21 closed sensor misaligned
Gripper air pressure low
Valve Y4 not switching
Jaws mechanically jammed
B21 cable / connector fault
Each has predicted test outcomes; tests carry reliability and safety preconditions.
Notes: The cell runs a fixed PLC sequence. At step 30 the close command Y4 is on but the closed sensor B21 never confirms within 1.5 s, so the PLC raises A-301 and stops. The operator sees only the stop. ARIA's job is to tell which of five physical causes is behind the same alarm, using machine evidence and safe tests. All plant data in the demo is simulated.

## Slide 2: GPT-Live talks, reasoning models investigate
OpenAI stack
Operator / technician
hands-free headset
browser mic
WebRTC
audio
GPT-Live · gpt-live-1
full-duplex voice (marin)
listens while it speaks
live-delegation of real work
delegate(task)
first words
commentary.append
+ thinking
OpenAI Agents SDK
ARIA agent · streamed run
strict function tools
operator inbox for mid-task remarks
gpt-5.6-terra
reasoning agent — hypotheses, test choice, report writing
gpt-5.6-luna
fast model — rerank, grounding audit, temporal fact extraction, titles
text-embedding-3-large
manual chunks + incident memory vectors
Responses API · structured outputs
typed JSON for plans, facts and reports
Evals · GPT-Live ↔ GPT-Live
simulated caller voice relay + gpt-5.6-terra judge
Streaming UI · Next.js
SSE events → live tool steps (“Worked for 6s”), generative cards via show_visual, Debug lanes: audio · transcript · delegation · tools · commentary
Notes: GPT-Live owns the conversation over WebRTC. The moment it hears real work it delegates to the backend; the Agents SDK runner streams the ARIA agent on gpt-5.6-terra. Luna handles the cheap, fast jobs; text-embedding-3-large backs both the manual RAG and the incident memory. Results go back into the call as commentary to speak and thinking for background. The same stack powers the evals: a simulated GPT-Live caller talks to ARIA and terra grades the transcript.

## Slide 3: One bounded loop — the model proposes, the engine decides
Inside ARIA
no → next test
Gather evidence
snapshot · alarms
sequence trace
Hypotheses
fault model + history
starting likelihoods
Select test
max information gain
safety preconditions
Run test
simulated PLC
real result returned
Bayesian update
for / against
rule out < 2 %
Stop rule?
yes
Write → verify → speak
refs · tests · confidence
+ luna grounding audit
Engine rules (code, not prompt)
stop at ≥ 90 % with support and no contradiction · or no safe test left · or budget / timeout → “uncertain, call a technician” · operator remarks are capped evidence
Strict function tools the loop calls
Knowledge RAG
BM25 + embeddings
RRF fusion → luna rerank
section citations
Temporal KB
incident timelines
facts: static · event · state
valid_from / valid_to
Safety policy
motion tests need robot home
no restart · reset · bypass
every request logged
CMMS
maintenance plan
overdue tasks
work orders + evidence
Generative UI
show_visual cards on ask
investigation card
debug timeline
Notes: Gather evidence, register hypotheses from the fault model, pick the permitted test with the highest information gain, run it against the simulated PLC, update every hypothesis with the real result, and check the stop rules. No → next test. Yes → write the report, re-read and verify it, then GPT-Live speaks it. The stop thresholds, safety preconditions and verification checks are in code, so the model cannot talk its way past them.