## Slide 1: Why did the palletizer stop?
Technical use case
The cell. A robotic palletizing cell stacks cases at the end of a packaging line. A PLC runs a fixed sequence and checks every step with a sensor before moving on.
The stop. At step 30 the gripper is told to close — valve Y4 is on — but the closed sensor B21 never confirms. After 1.5 seconds the PLC raises alarm A-301 and stops the cell.
The real problem. One alarm, five physical causes: a misaligned sensor, low air, a valve that won't switch, jammed jaws or a cable fault. Working out which one is where the downtime goes.
ARIA's job. Find the cause from machine evidence and safe tests, then tell the operator the next safe step — by voice, hands-free. ARIA never restarts or bypasses equipment.
SEQUENCE
Infeed
S10
Robot pick
S20
Gripper close
S30
Place
S40
A-301
Gripper close timeout · cell in FAULT
Y4
close command
ON
B21
closed feedback
OFF
T30
condition timer
> 1.5 s
CANDIDATE CAUSES
Sensor offset
Low air
Valve stuck
Jaws jammed
Cable fault
Notes: The cell runs a fixed PLC sequence. At step 30 the close command Y4 is on but the closed sensor B21 never confirms within 1.5 s, so the PLC raises A-301 and stops. Five physical causes produce the same alarm. ARIA's job is to tell which one from machine evidence and permitted tests, and say the next safe step. All plant data in the demo is simulated.

## Slide 2: One voice, a team of specialist models
OpenAI stack
Voice. GPT-Live (gpt-live-1) talks with the worker. It is full duplex — it listens while it speaks — and delegates real work the moment it hears it.
Reasoning. The OpenAI Agents SDK runs the ARIA agent on gpt-5.6-terra, which plans the investigation, chooses tests and writes the report.
Speed and knowledge. gpt-5.6-luna handles the fast jobs: reranking, grounding audits and fact extraction. text-embedding-3-large powers search across manuals and incident memory.
Back into the call. Results are injected as commentary to speak and thinking to know, so the worker is never left in silence.
Voice
gpt-live-1
WebRTC
live delegation
Orchestration
Agents SDK
streamed runs
strict tools
Reasoning
gpt-5.6-terra
gpt-5.6-luna
Responses API
Knowledge
text-embedding-3-large
hybrid RAG
temporal KB
Quality
GPT-Live caller
terra judge
safety scores
Notes: Top to bottom: GPT-Live is the voice and delegates work; the Agents SDK orchestrates the ARIA agent; terra reasons, luna does the fast jobs, structured outputs keep everything typed; embeddings back the manual search and the incident memory; and evals use a simulated GPT-Live caller with terra as the judge.

## Slide 3: An investigation, not a chatbot
Inside ARIA
Understand. GPT-Live hears the problem and hands it to ARIA straight away.
Gather. Machine snapshot, alarm history, sequence trace, the manual and past incidents on this line.
Reason. Hypotheses with evidence for and against. The engine runs the safe test that separates them most.
Decide. Stop at 90% confidence with supporting evidence — or say it is uncertain and call a technician.
Report. Written from tool results, verified against them, then spoken. Restart, reset and bypass are always declined.
ARIA
engine
1 Gather
2 Hypothesize
3 Pick safe test
4 Run test
5 Update belief
6 Verify & speak
Rule out < 2%
Stop ≥ 90%
Budget + timeout
Report verified
Notes: The loop runs clockwise: gather evidence, register hypotheses, pick the permitted test with the highest information gain, run it, update every hypothesis with the real result, and once a stop rule is met, write and verify the report before GPT-Live speaks it. The thresholds, safety preconditions and verification checks live in code — the model proposes, the engine decides.